## Slide 1
DEEPGRID SEMI · DG32-2DOM · SEPTEMBER 2026
Condition monitoring on the motor-control chip
The DG32-LITE lockstep motor-control SoC plus an INT8 attention engine on a second, 114 MHz clock · 130 nm CMOS · design complete, in physical trials
TWO CLOCK DOMAINS · ILLUSTRATIVE
114 MHz
COMPUTE CLOCK
Bit-exact
TO THE SOFTWARE MODEL
~3,242
CYCLES PER ROW, ANALYTIC
Same pinout
AS DG32-LITE, QFN-64
Pre-silicon: post-route, simulated and analytic values, each labelled where it appears.
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
01
Notes: DG32-2DOM is the attention variant of Deepgrid Semi's DG32-LITE motor-control chip. It keeps the dual-core lockstep controller and adds an INT8 attention engine on its own clock, so a drive can watch its own motor for faults. The design is complete and in physical trials. Every figure here is a post-route, simulated or analytic value, and each one is labelled.

## Slide 2
02 · EXECUTIVE SUMMARY
DG32-2DOM adds an INT8 engine, not a new core
DG32-2DOM in one slide: what is added, what is untouched, and what the engine costs
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
02
THE ANSWER
DG32-2DOM is DG32-LITE plus an INT8 attention engine on its own clock, added behind bridges so the lockstep control core is untouched.
Both chips come from one design source. The variant is a build option plus a second clock, on its own 3.4 × 4.5 mm die.
Status: design complete, in physical trials
114 MHz
COMPUTE CLOCK
The control domain stays at 50 MHz
400 keys
PER ATTENTION HEAD
Key dimension ≤ 32 bytes, value ≤ 64 bytes
~3,242
CYCLES PER QUERY ROW
Analytic, at 16 lanes and 400 keys
0 pads
ADDED TO THE PINOUT
Same QFN-64 as DG32-LITE
Sources: DG32-2DOM block architecture §1, §4.18; DG32-2DOM preliminary datasheet §1–2.
Notes: Here is the answer on one slide. DG32-2DOM is DG32-LITE plus an attention engine, not a new core. The lockstep CPU pair, boot path, peripherals and sixty-four-pin pinout are identical. The engine runs at one hundred fourteen megahertz, its output is bit-exact to the software model, and one query row costs about thirty-two hundred cycles, by analysis.

## Slide 3
03 · DESIGN PREMISES
Three findings forced a second clock domain
Each finding came from hardening the design, and each one set the variant’s shape
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
03
FINDING
WHAT IT MEANS
WHAT THE DESIGN DOES
Lockstep core fmax ~55–62 MHz
Raising the whole die clock would break the core’s timing
The control domain stays at 50 MHz
The engine is the throughput consumer
It needs more speed than the control core can give
The engine runs on its own 114 MHz clock
Engine memory congested the LITE floorplan
Adding its buffers made routing time out
DG32-2DOM gets its own 3.4 × 4.5 mm die
INT4 output came out identically zero
A 1/400 softmax weight rounds to zero at 4 bits
15-bit weights into a 40-bit numerator
Additions only
The frozen control core, boot path and bus decode are unchanged; the engine is added around them.
Source: DG32-2DOM block architecture §2, design premises and locked decisions.
Notes: Three findings forced the design. The lockstep core tops out around fifty-five to sixty-two megahertz, so the control domain has to stay at fifty. The engine is the throughput consumer, so it gets its own faster clock. And adding its memory to the DG32-LITE floorplan made routing time out, so the variant gets a larger die of its own.

## Slide 4
04 · ARCHITECTURE
The engine sits beside the core, behind bridges
Two clock domains on one die; the engine reaches memory only through the clock bridges
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
04
50 MHz control domain
Lockstep CPU pair
Fault latch + supervision
Boot ROM + SRAM
DMA + interrupts
Motor drive + sensing
Connectivity + test
Clock bridges
Lite
programming
Burst read
keys, values in
Burst write
output back
114 MHz compute domain
INT8 attention engine
Multiply · weight · combine · requantise · write back
K buffer · SRAM macro
V buffer · SRAM macro
EXP table · 256 × 15-bit
One 3.4 × 4.5 mm die · same QFN-64 pinout · pre-silicon design
1
One design source
A build option plus a second clock, not a fork.
2
Bridges only
The engine reaches memory only through the bridges.
3
Cannot stall
No engine transaction extends the core’s worst case.
4
Done interrupt
Completion reaches both cores as an interrupt.
Sources: DG32-2DOM block architecture §3, §4.18–4.19, §7 communication matrix.
Notes: This is the architecture. On the left, the fifty megahertz control domain: everything in DG32-LITE. On the right, the one hundred fourteen megahertz compute domain: the attention engine and its key and value buffers. Between them sit three clock-domain bridges. The engine reaches memory only through those bridges, so it can never stall the control core.

## Slide 5
05 · SHARED BASE
Everything proven on DG32-LITE carries over
The same blocks from the same design source; only the clocks change
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
05
BLOCK GROUP
ON DG32-LITE
ON DG32-2DOM
Lockstep safety core
MAIN + CHECKER, fault latch, FAULT_N
Identical
Boot and memory
64 KB ROM, 32 KB SRAM, external QSPI flash
Identical; the SRAM idle read port can feed the engine
Motor drive and sensing
PWM + brake, DShot × 4, encoder, ADC, CORDIC
Identical
Control-loop budget
~300 hardware cycles, ~100 kHz simulated
Identical
Package and pinout
QFN-64, 44 signal pins
Identical; the engine adds no pads
Clocks
One 50 MHz domain
50 MHz control + 114 MHz compute
The DG32-LITE deck and film cover the shared base in depth. This deck covers only what DG32-2DOM adds.
Sources: DG32-2DOM block architecture §1, §4.1–4.17, §5.1–5.2; DG32-2DOM preliminary datasheet §2.
Notes: Everything proven on DG32-LITE carries over unchanged. The lockstep pair, fault latch, boot ROM, SRAM, motor drive, sensing and connectivity are the same blocks from the same design source. The control loop still costs about three hundred hardware cycles, and the package is the same nine-by-nine millimetre QFN, because the engine adds no pads.

## Slide 6
06 · ATTENTION ENGINE
One kick computes a band of query rows
Every stage runs on the 114 MHz clock; firmware only programs the shapes and waits for done
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
06
Program
Shapes over AXI-lite
Multiply
QKᵀ, 16 lanes
Weight
Row max → EXP table
Combine
Sum ÷ one reciprocal
Requantise
Saturate to INT8
Write back
Output to memory
Bit-exact
Every output matches the golden software model, for any geometry the engine accepts.
Reuse between kicks
A later kick can skip the load and reuse resident keys, values and the weight table.
One multiply array
The same array serves the key pass and the value pass, keeping the datapath small.
Up to 400 keys per head · key dimension up to 32 bytes · value dimension up to 64 bytes
Sources: DG32-2DOM block architecture §4.18; DG32-2DOM preliminary datasheet §1, §8.
Notes: One kick computes a band of query rows of one attention head, end to end. Firmware programs the shapes. A shared multiply array computes Q times K transpose. A row maximum indexes a table of softmax weights. The engine forms the weighted sum, divides once per row, saturates the result to INT8, and writes the output back to memory.

## Slide 7
07 · PRECISION
INT4 rounded every weight to zero
With about 400 near-uniform keys, each softmax weight is close to 1/400
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
07
1/400
ONE SOFTMAX WEIGHT
About 0.0025 with ~400 near-uniform keys
0
WHAT INT4 KEPT
The weight rounded to zero; the output came out identically zero
~82 levels
WHAT 15 BITS KEEP
Derived: 32,767 ÷ 400
Weights stay unquantised
Fifteen-bit weights run all the way into the numerator; only the final output is saturated to INT8.
A 40-bit numerator
A 32-bit numerator breaks at 512 keys. Forty bits stays exact to 131,072 keys, so bit-exactness holds.
Source: DG32-2DOM block architecture, locked decisions and §4.18 rationale. Level count derived.
Notes: Why INT8, and not INT4? With about four hundred similar keys, each softmax weight is close to one four-hundredth. INT4 rounds that to zero, and the output came out identically zero. The engine keeps fifteen-bit weights all the way into a forty-bit numerator, which stays exact to more than one hundred thousand keys, and it saturates only the final output.

## Slide 8
08 · MEMORY TRAFFIC
Loading keys and values once cuts traffic 400×
Bus traffic per attention head, drawn to scale: resident buffers against streaming values per row
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
08
KEYS AND VALUES RESIDENT, RE-READ PER ROW
~1% bus occupancy
VALUES STREAMED FOR EVERY ROW
~400× the traffic
Relative scale: both bars share one axis, so the resident case is a sliver.
Load once, re-read per row
Keys and values sit in SRAM macros beside the engine and are re-read for every query row.
A contention-free feed
A DMA and the SRAM’s idle second read port can move data to the engine without the CPU.
Why it matters
Streaming would make the engine fight the rest of the die for memory.
Source: DG32-2DOM block architecture §4.18 rationale, §4.3, §4.17.
Notes: Memory traffic decides whether the engine fights the rest of the chip. Keys and values load once per kick and are re-read for every query row, which keeps one head's bus traffic around one percent. Streaming the values row by row would cost about four hundred times that. A DMA and the SRAM's idle read port can feed the engine without contending with the CPU.

## Slide 9
09 · CLOCK BRIDGES
Rare crossings let a handshake replace a FIFO
Every transaction between 50 MHz and 114 MHz crosses a four-phase level handshake
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
09
50 MHz side
CPU and DMA traffic
Request
Payload held stable
2-flop sync
Metastability guard
Acknowledge
4-phase handshake
114 MHz side
Attention engine
Lite bridge
Carries programming, with one transaction outstanding at a time.
Burst read bridge
Batches a whole read burst into a single crossing.
Burst write bridge
Batches a whole write burst into a single crossing.
Why not a FIFO
Keys and values load once and outputs write back once, so a small, provably safe handshake needs no gray-coded pointers.
Source: DG32-2DOM block architecture §4.19.
Notes: Crossings between the two clocks are rare: keys and values load once, and outputs write back once. So the bridges use a small four-phase handshake through two-flop synchronisers instead of a FIFO. One bridge carries programming, one transaction at a time, and two burst bridges batch a whole read or a whole write into a single crossing.

## Slide 10
10 · ENGINE COST
One query row costs about 3,242 cycles
Analytic, at 16 lanes, 400 keys, 32-byte keys and 64-byte values; the bench figure comes at bring-up
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
10
TERM
HOW IT SCALES
CYCLES
Value pass
keys × value dim ÷ lanes
1,600
Key pass
keys × key dim ÷ lanes
800
Requantise
11 × value dim
704
Write back + drain
remainder
~90
Divide
48-step restoring
48
~3,242 cycles
PER QUERY ROW
Analytic; the steady-state bench measurement is a bring-up item
The value pass dominates
Half of each row is the weighted sum over the values; the key pass is a quarter.
ONE QUERY ROW, DRAWN TO SCALE (~3,242 CYCLES)
Values 49%
Keys 25%
Requantise 22%
Source: DG32-2DOM block architecture §4.18, analytic cost. Term split and shares derived; write back + drain = 3,242 − 3,152.
Notes: Here is what one query row costs, by analysis, at sixteen lanes, four hundred keys, thirty-two-byte keys and sixty-four-byte values. The value pass is the largest share, at sixteen hundred cycles. The key pass takes eight hundred, requantisation about seven hundred, and the divide forty-eight. That totals about thirty-two hundred and forty cycles. The measured figure comes at bring-up.

## Slide 11
11 · TIMING AND DIE
Both clocks close timing on a larger die
Post-route results on the 130 nm process; silicon measurements follow bring-up
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
11
+0.30 ns
SLACK AT 50 MHZ
Control domain, post-route
+0.19 ns
SLACK AT 114 MHZ
Compute domain, post-route
3.4 × 4.5 mm
DIE
Its own die, not the DG32-LITE slot
55–62 MHz
LOCKSTEP CORE FMAX
Why control stays at 50 MHz
What is closed
Post-route timing at both clocks, and an engine that is bit-exact against the software model.
What is still to measure
Steady-state cycles per query row on a bench, and every figure on fabricated silicon.
Sources: DG32-2DOM block architecture §5.3; DG32-2DOM preliminary datasheet §10.
Notes: Both domains close timing on the larger die. The fifty megahertz control domain closes with zero point three nanoseconds of slack, and the one hundred fourteen megahertz compute domain with zero point one nine. The die is three point four by four point five millimetres. These are post-route results; silicon measurements follow bring-up.

## Slide 12
12 · USE AND ROADMAP
The engine targets bearing faults in the drive
Condition monitoring on the chip that already turns the motor, and where it sits on the roadmap
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE · SEPTEMBER 2026 · PRE-SILICON
12
Bearing-fault detection
Runs in the drive itself, on the chip that already turns the motor.
Anomaly detection
Flags abnormal drive behaviour without adding a second processor to the board.
DIMENSION
DG32-2DOM
STM32G0
On-chip AI
INT8 attention engine in hardware
None; NanoEdge AI runs in software
Control core
Lockstep RISC-V pair, untouched
Single Cortex-M0+
NOW
DG32-LITE first silicon
September 2026 shuttle
NOW
DG32-2DOM
Design complete, in physical trials
AT BRING-UP
Measure the engine
Cycles per query row on a bench
NEXT SPIN
Close the gaps
12-bit ADC and embedded flash
Sources: DG32-LITE investor block diagram p1–p2; DG32-2DOM block architecture §4.18.
Notes: The engine is designed for condition monitoring inside the drive: bearing-fault and anomaly detection, on the chip that already turns the motor. Against the STM32G0, which runs AI in software, that is a hardware differentiator. It sits on the roadmap alongside DG32-LITE first silicon, with its own design complete and in physical trials.

## Slide 13
13 · CLOSE
AI in the drive. Control left untouched.
Next milestone: bring-up measures the engine’s cycles per query row and turns these design values into measurements.
THREE THINGS TO REMEMBER
1 · An addition, not a redesign
The engine and bridges are added around the frozen lockstep core, boot path and bus decode.
2 · Exact arithmetic
INT8 output, bit-exact to the software model, with no weight rounded to zero.
3 · Cost known before silicon
About 3,242 cycles per query row by analysis, with timing closed at 50 MHz and 114 MHz.
DEEPGRID SEMI · DG32-2DOM ARCHITECTURE
13
Notes: Three things to take away. The engine is an addition, not a redesign: the safety core is untouched. Its arithmetic is exact: INT8 output, bit-exact to the model, with no weight rounded to zero. And its cost is known before silicon: about thirty-two hundred cycles per query row. First silicon turns these design values into measurements.