## Slide 1
DEEPGRID SEMI · DG32-LITE · PRELIMINARY DATASHEET
A lockstep motor MCU in a QFN-64 package
The preliminary datasheet at overview level, for hardware and firmware leads · design values and process nominals, pending first-silicon characterisation
QFN-64 · ILLUSTRATIVE
9 × 9 mm
QFN-64 BODY
44
SIGNAL PINS
1.8 / 3.3 V
CORE / I/O RAILS
50 MHz
ONE CLOCK DOMAIN
Preliminary, pre-silicon. Register maps, the memory map and board-design rules are in the engineering datasheet, not this deck.
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
01
Notes: DG32-LITE is Deepgrid Semi's lockstep RISC-V motor-control chip, and this is its preliminary datasheet in twelve slides. Two cores run in lockstep inside a nine-by-nine millimetre, sixty-four-pin QFN. Everything here comes from the design as built for first silicon and from process nominals, not from measured parts, and each slide says which is which.

## Slide 2
02 · DESIGN-IN
Four facts set every DG32-LITE design-in
Rails, clock and pins: the parts of the datasheet a design commits to first
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
02
1.8 V
CORE RAIL
Logic, SRAM and the ADC · 1.71–1.89 V
3.3 V
I/O RING
Pads and ESD · 3.0–3.6 V
50 MHz
CLOCK
One domain, no on-die PLL
44 / 64
SIGNAL PINS
Twenty supplies and grounds
Everything else in the datasheet follows from these four facts: which rails to provide, which clock to route, and which pins the drive, the flash and debug take.
Rails
Four required rails; unused rails tied to nominal.
Clock
One 3.3 V CMOS input, no PLL; core ~55–62 MHz.
Pins
44 signals in eleven groups; 20 supplies and grounds.
Source: DG32-LITE preliminary datasheet §2, §4.1, §5, §6.1.
Notes: Four facts set every design-in. The core runs from a one point eight volt rail. The input and output ring runs at three point three volts. The whole chip runs from one fifty megahertz clock. And every signal comes out through forty-four pins of a sixty-four-pin package, with the other twenty pins given to supplies and ground.

## Slide 3
03 · FEATURES
Nine features, one self-booting safety SoC
The datasheet’s feature list, grouped as a design sees it
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
03
Lockstep cores
Two RV32IM cores, a fault comparator and a sticky fault register
Memory
32 KB SRAM, 64 KB boot ROM and a window onto external flash
3-phase PWM
Complementary, programmable dead-time, hardware brake
DShot × 4
Four ESC channels, pin-muxed onto the PWM pads
Position and math
Quadrature and Hall with timestamps; CORDIC for FOC
On-die ADC
8-bit differential SAR, triggered by the PWM
Connectivity
Two UARTs, an SPI master, an I²C master and GPIO
Supervision
Two timers, a windowed watchdog and a supply supervisor
Self-boot
No management core; an unmapped access returns an error
Source: DG32-LITE preliminary datasheet §1, features.
Notes: The datasheet lists nine features. Two RISC-V cores in lockstep with a fault comparator. Thirty-two kilobytes of SRAM and a sixty-four kilobyte boot ROM. Three-phase PWM with a hardware brake, four DShot channels, encoder and Hall inputs, a CORDIC and an on-die ADC. Serial ports, SPI, I squared C and GPIO, with supervision. And it boots itself, with no management core.

## Slide 4
04 · PIN GROUPS
44 signal pins in eleven functional groups
Every signal pin by function; the remaining 20 pins are supplies and grounds
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
04
GROUP
SIGNALS
PINS
Motor PWM
AH, AL, BH, BL, CH, CL + ADC trigger
7
QSPI flash
Clock, 4 data, 2 chip selects
7
Position
Encoder A, B, Z · Hall A, B, C
6
Serial
UART0 TX/RX · UART1 TX/RX
4
SPI
SCLK, MOSI, MISO, CSN
4
JTAG
TCK, TMS, TDI, TDO
4
GPIO
GPIO0–2
3
Safety
FAULT_N · 2 × supply-good inputs
3
Analog
SAR ADC VINP, VINN (0–1.8 V)
2
I²C
SCL, SDA (open-drain)
2
Clock & reset
CLK, RST_N
2
PINS PER GROUP, TO SCALE
Motor PWM
7
QSPI flash
7
Position
6
Serial
4
SPI
4
JTAG
4
GPIO
3
Safety
3
Analog
2
I²C
2
Clock & reset
2
Source: DG32-LITE preliminary datasheet §3, §3.1 pins by function.
Notes: Forty-four signal pins fall into eleven groups. Motor PWM and its sample trigger take seven, and so does the QSPI flash. Position sensing takes six. Serial, SPI, JTAG and GPIO take fifteen between them. Three carry safety signals, including the fault output, and the analog inputs, I squared C, and clock and reset take two each.

## Slide 5
05 · PIN PLACEMENT
Each side of the package groups related signals
Supplies and grounds sit between the groups on every side; pin 1 is upper left, numbered counter-clockwise
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
05
DG32-LITE
QFN-64 · TOP VIEW · PIN 1 ●
Top · pins 49–64 · I²C, GPIO and safety
SPI MISO and CSN · I²C · GPIO0–2
FAULT_N · supply-good × 2 · ADC +
Left · pins 1–16 · Motor and position
PWM AH, AL, BH, BL, CH, CL
PWM trigger
Encoder A, B, Z · Hall A, B
ADC −
Right · pins 33–48 · Flash and serial
QSPI CSN0, IO0–3, CSN1
UART0 TX/RX · UART1 TX/RX
SPI SCLK and MOSI
Bottom · pins 17–32 · Debug, clock and reset
JTAG × 4 · CLK · RST_N and resetb · Hall C · QSPI clock
Source: DG32-LITE preliminary datasheet §2–3. Pin map awaiting the foundry’s bond-diagram confirmation.
Notes: The pins are placed by job. One side carries the motor: all six gate outputs, the sample trigger, the encoder and two Hall inputs. The opposite side carries the boot flash and the serial ports. The bottom holds JTAG, the clock and the resets, and the top holds I squared C, GPIO, the fault output and the supply-good inputs.

## Slide 6
06 · ELECTRICAL
Every electrical limit is a nominal until silicon
Recommended operating conditions and absolute maximums, before characterisation
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
06
PARAMETER
SYMBOL
MIN
TYP
MAX
UNIT
NOTE
Core supply
vccd1
1.71
1.8
1.89
V
±5%; logic, SRAM and the ADC
I/O supply
vddio
3.0
3.3
3.6
V
3.3 V CMOS pad ring and ESD
Core clock
CLK
–
50
~55
MHz
fmax ~55–62 MHz post-route
ADC input
VINP / VINN
0
–
1.8
V
Differential, core domain
Junction temp
TJ
–
25
–
°C
Range set at characterisation
ABSOLUTE MAXIMUM
MIN
MAX
UNIT
Core supply vccd1
−0.3
1.95
V
I/O supply vddio
−0.3
3.63
V
Any digital pad
−0.3
vddio + 0.3
V
Analog pad
−0.3
vccd1 + 0.3
V
Storage temperature (target)
−40
125
°C
Why every row is provisional
These are process nominals for this die’s supply domains. First-silicon characterisation replaces the section.
Source: DG32-LITE preliminary datasheet §4.1–4.2. Absolute maximums are process limits, pre-characterisation.
Notes: Every electrical limit in this datasheet is a design target or a process nominal, and first-silicon characterisation will replace it. The core supply runs from one point seven one to one point eight nine volts, and the input and output supply from three to three point six. The analog inputs accept zero to one point eight volts, and absolute maximums sit just above the operating range.

## Slide 7
07 · POWER
All logic draws from one 1.8 V rail
Which rails are required, which are tie-offs, and the order they come up
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
07
RAIL
PINS
VOLTAGE
ROLE
vccd1
49
1.8 V
Logic, SRAM, ADC · required
vddio
17, 64
3.3 V
Pad ring and ESD · required
vccd
18
1.8 V
Wrapper core · required
vdda
30
3.3 V
Analog, POR · required
vdda1, vdda2
9, 40, 47
3.3 V
Unused · tie to 3.3 V
vccd2
63
1.8 V
Unused · tie to 1.8 V
Grounds
8 pins + paddle
0 V
Every vss pin and the paddle
Every milliamp of dynamic and leakage current is drawn from vccd1.
~0.43 W
AT 50 MHZ
Tool estimate at 25 °C and 1.8 V, not measured
Sequencing
3.3 V comes up before or together with 1.8 V.
Why unused rails are tied
Nominal voltage keeps the pad ring’s protection structures biased.
Source: DG32-LITE preliminary datasheet §4.3, §5 power supplies and sequencing.
Notes: Power is simple. All logic, memory and the ADC draw from the one point eight volt user rail. The other user rails are unused, and are tied to their nominal voltage only to keep protection structures biased. Bring up three point three volts before or together with one point eight. The tool estimate is about zero point four three watts at fifty megahertz.

## Slide 8
08 · CLOCK AND RESET
One clock pin, two resets and no PLL
The whole die runs from one clock as delivered; any reset input resets the core
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
08
CLK pin
3.3 V CMOS, 50 MHz target
No PLL
Clock used as delivered
One domain
CPU and every peripheral
resetb
Active low, 3.3 V
RST_N
Active low, external
Power-on reset
From the wrapper
Combined on die
Any one resets the core
Use either reset
Both are combined on the die; pull the unused input high.
Measured ceiling
The lockstep core reaches ~55–62 MHz post-route, so 50 MHz is the target.
Source: DG32-LITE preliminary datasheet §6.1, §4.1.
Notes: Clocking is just as direct. One three point three volt clock input drives the whole chip at a fifty megahertz design target, and there is no on-die PLL. Two active-low resets are combined on the die with the power-on reset, so a board can use either one and pull the other high. The core itself reaches fifty-five to sixty-two megahertz after place-and-route.

## Slide 9
09 · BOOT
The ROM boots from flash or opens a monitor
Standalone boot: no management core, no external help
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
09
Banner
UART0 at 115,200 baud, 8N1
Check header
Reads the flash image header
Copy
Quad-SPI read into SRAM
Run
Jumps to the copied image
Blank flash
A UART monitor with read, write, jump and info commands starts instead.
Code runs from SRAM
Nothing executes in place from external flash; executable code belongs in SRAM.
64 KB
BOOT ROM
Runs with no external help
115,200
CONSOLE BAUD
Divider fixed for 50 MHz
Quad SPI
FLASH READ
Image copied into SRAM
Source: DG32-LITE preliminary datasheet §6.2 boot flow.
Notes: The chip boots with no outside help. The ROM prints a banner on the console UART, reads and checks the flash image header, copies the image into SRAM over a quad-SPI read, and jumps to it. Code runs from SRAM, not in place from flash. If the flash is blank, a UART monitor starts instead, so a bare board can still be inspected.

## Slide 10
10 · PERIPHERALS
Peripheral limits a firmware plan can rely on
Capability and timing per block, from the datasheet’s block notes
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
10
BLOCK
LIMIT
NOTE
UART × 2
115,200 baud, 8N1 at 50 MHz
Writes wait while busy; a byte is never dropped
SPI master
Up to 25 MHz
0.64 µs per 16-bit word
I²C master
100 / 400 kHz, 7-bit addressing
Clock stretching; a 2-byte read takes ~72 µs at 400 kHz
3-phase PWM
Dead-time up to 5.1 µs at 50 MHz
Hardware brake forces all six outputs off in ≤ 2 cycles
DShot × 4
16-bit frames with CRC4
All four channels share one bit-time counter
Encoder + Hall
4× quadrature, index, 3 Hall inputs
Edge timestamps give velocity at low speed
SAR ADC
8-bit differential, ~200 kSa/s
Trim taps unrouted: runs untrimmed on this silicon
CORDIC
sin, cos, atan2, magnitude
20 iterations, ~53–58 cycles per operation
DMA
~7.1 cycles per word moved
The CPU keeps bus priority
Source: DG32-LITE preliminary datasheet §1 and §8 block notes (capabilities only, no register detail).
Notes: These are the limits firmware can plan on. The UARTs run at one hundred fifteen thousand two hundred baud, SPI to twenty-five megahertz, and I squared C at one hundred or four hundred kilohertz. PWM dead-time reaches five point one microseconds, and the brake acts within two cycles. The ADC samples at about two hundred kilosamples per second, and on this silicon it runs untrimmed.

## Slide 11
11 · PACKAGE AND STATUS
The package is final; the pin map is preliminary
What a design can lock now, and what waits for first silicon
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET · SEPTEMBER 2026 · PRE-SILICON
11
9 × 9 mm
QFN-64 BODY
64 pins
0.5 mm
PITCH
Standard QFN lead pitch
Ground
EXPOSED PADDLE
Solder to the ground plane
Pin 1
UPPER LEFT
Numbered counter-clockwise
Preliminary: pin map
Awaiting the foundry’s bond-diagram confirmation.
Preliminary: electrical limits
Process nominals until first-silicon characterisation.
Frozen: the control core
Closed for feature work until silicon test.
130 nm CMOS · QFN-64 · first silicon on the September 2026 multi-project shuttle
Source: DG32-LITE preliminary datasheet §10 package and header notes.
Notes: The package is settled: a nine-by-nine millimetre QFN with a half-millimetre pitch and an exposed ground paddle. Three things are still preliminary. The pin map waits on the foundry's bond-diagram confirmation, the electrical section waits on characterisation, and the control core stays frozen for feature work until silicon test.

## Slide 12
12 · CLOSE
Fixed now. Measured at first silicon.
Register maps, the memory map and board-level rules live in the engineering datasheet, not in this overview.
THREE THINGS TO REMEMBER
1 · Fixed: package and pins
QFN-64, 9 × 9 mm, with 44 signals in eleven groups and pin 1 upper left.
2 · Fixed: rails, clock, boot
A 1.8 V core, a 3.3 V I/O ring, one 50 MHz clock and self-boot from flash.
3 · Measured next
Every electrical limit, and the final pin map, at first-silicon characterisation.
DEEPGRID SEMI · DG32-LITE PRELIMINARY DATASHEET
12
Notes: So here is what is fixed and what is not. Fixed now: the package, the pin groups, the rails, the clock and the boot path. Measured at first silicon: every electrical limit, and the final pin map. The register-level detail lives in the engineering datasheet; this deck is the plan you build around.