## Slide 1
DEEPGRID SEMI · DG32-LITE · TAPE-IN BLOCK DIAGRAM
DG32-LITE as built for tape-in
The die as recorded in its tape-in block diagram · one clock domain, 130 nm CMOS · a design record, not a measurement of silicon
QFN-64 · ILLUSTRATIVE
2.9 × 4.5
MM CORE BLOCK
44
PADS, ALL ALLOCATED
18
BLOCKS ON THE BUS
4
SIGN-OFF GATES
Design state September 2026. This deck lists the sign-off gates; it makes no claim that they have passed.
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
01
Notes: This is DG32-LITE as recorded in its tape-in block diagram: the die as built, block by block. It covers the clock and reset, the lockstep pair, memory and fetch, the bus and the eighteen blocks around it, the pad plan, production test, and the four sign-off gates the die must pass. It is a design record, not a measurement of silicon.

## Slide 2
02 · EXECUTIVE SUMMARY
One clock, 44 pads, and four gates before tape-in
What the tape-in diagram records about the die as built
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
02
50 MHz
ONE CLOCK DOMAIN
Core ceiling ~55–62 MHz, post-route
2 cycles
CHECKER DELAY
CHECKER sees MAIN’s bus responses
44 / 44
PADS ALLOCATED
Every wrapper pad has a job
4
SIGN-OFF GATES
All must pass on the final die
Safety
Lockstep pair with mirrored bus responses and a fault pad.
Bus
Two masters; gated or undecoded slots answer with an error.
Test
13 scan chains through JTAG; four gates before tape-in.
A single clock and reset, a lockstep pair that tolerates interrupts and peripheral reads, a two-master bus where nothing hangs, and a pad plan with no spare pin.
Source: DG32-LITE tape-in block diagram (state 2026-09-10).
Notes: The short version. One fifty megahertz clock domain, with the lockstep core measured at fifty-five to sixty-two megahertz after place-and-route. A checker that runs two cycles behind and sees the main core's bus responses. Forty-four wrapper pads, every one of them allocated. And four sign-off gates that must all pass on the final die.

## Slide 3
03 · CLOCKS AND RESET
One clock and one reset drive the whole block
Eight clock gates idle unused peripherals; test mode overrides them all
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
03
Clock pad
50 MHz, one domain
Eight clock gates
Idle peripherals switched off
Test mode
Forces every gate open
Reset pad
Asynchronous, active low
Supervisor
Deglitches supply-good inputs
MAIN, then CHECKER
Checker released two cycles later
Which peripherals can be gated
UART0, UART1, SPI, I²C, PWM, the timers, the DMA and the CORDIC.
Source: DG32-LITE tape-in block diagram, clocks and reset.
Notes: One clock and one reset drive the whole block. The clock arrives from a pad at fifty megahertz. Eight software clock gates switch off idle peripherals: both UARTs, SPI, I squared C, PWM, the timers, the DMA and the CORDIC. Test mode forces every gate open. Reset is asynchronous, the supervisor deglitches the supply-good inputs, and the checker leaves reset two cycles after the main core.

## Slide 4
04 · DUAL-CORE LOCKSTEP
The checker trails MAIN and sees its bus responses
The pair is arranged so ordinary firmware cannot make the two cores disagree
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
04
MAIN
Runs firmware, owns the bus
Two-cycle delay
Inputs and bus responses mirrored
CHECKER
Replays the same work
Compare stores
A mismatch sets a sticky fault
Interrupts are safe
One interrupt register feeds both cores, with the checker’s inputs delayed to match.
Peripheral reads are safe
Firmware may branch on a peripheral read; the checker sees the same response.
Verified in simulation
The lockstep pair is verified under interrupts in simulation.
A mismatch drives the FAULTn pad, so the fault reaches the board without firmware.
Source: DG32-LITE tape-in block diagram, dual-core lockstep.
Notes: The lockstep pair is built to survive real firmware. The main core runs the code and owns the bus. The checker replays the same work two cycles later, with its inputs and bus responses mirrored, and the comparator checks every committed store. So interrupts are safe, firmware may branch on a peripheral read, and the pair has been verified under interrupts in simulation. A mismatch drives the fault pad.

## Slide 5
05 · MEMORY AND FETCH
Code runs from SRAM through a dedicated fetch port
The fetch path is separate from the data bus, so fetch never waits on data traffic
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
05
Fetch decoder
Routes each fetch by region
ROM or SRAM
Boot to ROM; application to SRAM port 1
Anything else
Bus error, then instruction fault
Boot ROM
16,384 words of mask-programmed logic. Prints the banner, checks the flash header, copies the application and jumps.
SRAM, 32 KB
16 × 2 KB dual-port macros: port 0 for CPU and DMA data, port 1 for instruction fetch.
No valid flash header opens a UART monitor. The application installs its trap vector and enables interrupts.
Source: DG32-LITE tape-in block diagram, fetch decoder, boot ROM, SRAM and boot flow.
Notes: Code runs from SRAM through a dedicated fetch port. The fetch decoder sends boot fetches to the ROM and application fetches to the SRAM's second port. Anything else is a bus error and an instruction fault. The ROM is sixteen thousand words of mask-programmed logic that prints the banner, checks the flash header, copies the application and jumps. Blank flash opens a UART monitor.

## Slide 6
06 · ON-CHIP BUS
One requester at a time, and no access hangs
An AXI-lite bus with two masters and an error slave for every unanswered address
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
06
Two masters
CPU first, DMA second
Target latched
Held from request to response
32-bit slaves
Every block is a register slave
Error slave
Answers gated or undecoded slots
Gated means absent
A clock-gated peripheral decodes to the error slave, except in test mode.
Flash is a data window
The QSPI window serves data; the ROM copies code into SRAM.
2
BUS MASTERS
The CPU has priority over the DMA
32-bit
REGISTER SLAVES
Every peripheral on the bus
Error
FOR UNANSWERED SLOTS
By design, no access hangs
Source: DG32-LITE tape-in block diagram, AXI-lite bus.
Notes: The bus serves one requester at a time. The CPU has priority over the DMA, and each read or write target is latched at the request and held until the response. Every peripheral is a thirty-two-bit register slave. A clock-gated or undecoded slot answers with an error instead of hanging, and the QSPI window serves data, not code.

## Slide 7
07 · BLOCKS ON THE BUS
Eighteen blocks sit around the bus
Every peripheral is a 32-bit register slave on the same AXI-lite bus
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
07
UART0 · UART1
115,200 baud; UART0 is the console
SPI master
Up to 25 MHz
I²C master
100 / 400 kHz, 1–4 bytes
QSPI + window
NOR flash and PSRAM
GPIO × 3
In, out and enable per pin
Timers × 2
32-bit, compare interrupt
3-phase PWM
Dead-time, sample trigger, brake
DShot × 4
Steered onto the PWM pads
Encoder + Hall
4× quadrature, index, 3 Hall
CORDIC
20 iterations, Q1.31
ADC → SAR
8-bit differential, ~200 kSa/s
Interrupts
16 sources, software interrupt
System control
Part ID, 8 clock gates, pin mux
Watchdog
Windowed; supply-good deglitch
Fault register
Lockstep fault to FAULTn
Error slave
Undecoded or gated slots
Scan / DFT
13 scan chains
JTAG TAP
In the wrapper; reaches scan
Connectivity
Motor and sensing
System, safety and test
Source: DG32-LITE tape-in block diagram, slave slots.
Notes: Eighteen blocks sit around that bus. Six handle connectivity: the UARTs, SPI, I squared C, the QSPI window, GPIO and the timers. Six serve the motor: PWM, DShot, encoder and Hall, CORDIC, the ADC and interrupts. And six handle system, safety and test: system control, the watchdog, the fault register, the error slave, scan, and the JTAG port.

## Slide 8
08 · PAD PLAN
Every one of the 44 wrapper pads has a job
The wrapper’s pad plan (rev 2), grouped by function
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
08
ALL 44 WRAPPER PADS, BY GROUP, TO SCALE
QSPI 7
PWM 7
ENC + HALL 6
UART 4
SPI 4
JTAG 4
GPIO 3
GROUP
PADS
CARRIES
Clock
1
50 MHz clock in
QSPI flash
7
Clock, 4 data, 2 selects
UART0 / UART1
4
Console and telemetry
SPI
4
Master clock, data, select
I²C
2
Clock and data, open-drain
GPIO
3
General-purpose pins
FAULTn
1
Lockstep fault output
GROUP
PADS
CARRIES
Supply-good
2
Supervisor inputs
ADC
2
Differential analog inputs
PWM + trigger
7
Six gate outputs, ADC trigger
Encoder + Hall
6
A, B, Z and three Hall inputs
JTAG
4
TCK, TMS, TDI, TDO
Reset
1
Active-low reset in
The wrapper also holds the JTAG TAP and the power connections; the block and the wrapper are hardened in separate flows.
Source: DG32-LITE tape-in block diagram, wrapper pad plan (rev 2).
Notes: Every one of the forty-four wrapper pads has a job. Seven carry the QSPI flash, seven the PWM outputs and trigger, and six the encoder and Hall inputs. Four each go to the UARTs, SPI and JTAG. Three are GPIO. Two each carry I squared C, supply-good and the analog ADC inputs, and one each carry the clock, the reset and the fault output.

## Slide 9
09 · PRODUCTION TEST
Production test reaches 13 scan chains via JTAG
Scan serves manufacturing test; interactive CPU debug is a separate roadmap item
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
09
Tester
Drives the four JTAG pins
JTAG TAP
Scan enable, mode, chain select, bypass
13 scan chains
Through the hardened block
Test mode opens every gate
Clock gates are forced open and gated slots decode normally, so scan reaches every block.
Separate from debug
Scan is for production test; interactive CPU debug over JTAG is on the roadmap.
13
SCAN CHAINS
Inside the hardened block
4
JTAG PINS
TCK, TMS, TDI, TDO
All
CLOCK GATES OPEN
In test mode
Sources: DG32-LITE tape-in block diagram (scan/DFT, JTAG TAP); investor block diagram p2 (debug roadmap).
Notes: Production test reaches the logic through JTAG. A tester drives the four JTAG pins into a test access port in the wrapper, which selects scan enable, scan mode, a chain, or bypass, and reaches thirteen scan chains inside the hardened block. Test mode forces every clock gate open, so scan reaches every block. Interactive CPU debug over JTAG is a roadmap item.

## Slide 10
10 · SIGN-OFF GATES
Four gates must all pass before tape-in
Every gate runs on the final hardened die; passing three is not enough
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM · SEPTEMBER 2026 · PRE-SILICON
10
GATE 1
DRC clean
Every design rule, the whole die
GATE 2
LVS match
Circuits match uniquely, pins included
GATE 3
Connectivity
Every pad reaches logic; no floating net
GATE 4
Boot simulation
Routed netlist prints the banner
Why a connectivity gate
Design-rule and layout-versus-schematic checks can both pass while a pad pin floats. Only a pin-level check on the final layout catches it.
What this deck states
The gates the die must pass, not their results. It makes no tapeout-ready claim.
Source: DG32-LITE tape-in block diagram, sign-off gates.
Notes: Four gates must all pass before tape-in. The layout must be design-rule clean. Layout versus schematic must match uniquely, pins included. A connectivity check on the final layout must show every pad reaching logic, with no floating net. And a gate-level simulation of the routed netlist must boot and print the banner. The connectivity gate exists because the first two can pass while a pad pin floats.

## Slide 11
11 · CLOSE
Built to be checked, not assumed.
Next milestone: first silicon on the September 2026 multi-project shuttle.
THREE THINGS TO REMEMBER
1 · One clock, one reset
A single 50 MHz domain with eight clock gates and a checker released two cycles after MAIN.
2 · Nothing hangs, nothing floats
Gated or undecoded slots answer with an error, and all 44 pads are allocated.
3 · Four gates before tape-in
DRC, LVS, pin connectivity and a gate-level boot simulation must all pass.
DEEPGRID SEMI · DG32-LITE TAPE-IN BLOCK DIAGRAM
11
Notes: Three things to take away. One clock and one reset, with eight clock gates and a checker released two cycles late. Nothing hangs and nothing floats: bad accesses return errors, and all forty-four pads are allocated. And four gates stand between the design and tape-in. The next milestone is first silicon, on the September twenty twenty-six shuttle.